## Slide 1: Introduction to Model Driven Programmability
Srivatsa M B

## Slide 2: Agenda
The Road to Model Driven Programmability
Introduction to YANG Data Models
Introduction to NETCONF
Introduction to RESTCONF
Conclusion and Q/A
Note: All code samples referenced in this presentation are available at
https://github.cisco.com/XXX

## Slide 3: The Road to Model Driven Programmability

## Slide 4: IDEA?!!! what It would take to Configure 12,000 devices at one GO!!
Could be an Interpreter!! BASH?

## Slide 5: Could be SNMP?
SNMP works “reasonably well for device monitoring”
RFC 3535: Overview of the 2002 IAB Network Management Workshop – 2003 https://tools.ietf.org/html/rfc3535
Typical config: SNMPv2 read- only community strings
Typical usage: interface statistics queries and traps
Empirical Observation: SNMP is not used for configuration
  Lack of Writeable.
  Security Concerns
  Difficult to Replay/Rollback
  Special Applications
Simple Network Management Protocol (SNMP) is an application-layer protocol used to manage and monitor network devices and their functions.

## Slide 6: RFC 3535: What is Needed? Group to Decide the Next generation Network Programmability??
A programmatic interface for device configuration
Separation of Configuration and State Data
Ability to configure "services" NOT "devices"
Integrated error checking and recovery
What do we need?

## Slide 7: Model Driven Programmability New Methodology on Network?
NETCONF – 2006 – RFC 4741 (RFC 6241 in 2011)
YANG – 2010 – RFC 6020
RESTCONF – 2017 – RFC 8040
gRPC – 2015 – OpenSource project by Google

## Slide 8: Transport (Protocol) vs Data (Model)
NETCONF
RESTCONF
gRPC
YANG

## Slide 9: What is YANG?
YANG is a data modeling language for the NETCONF configuration management protocol. Together, NETCONF and YANG provide the tools that network administrators need to automate configuration tasks across multiple devices in a software-defined network (SDN).

## Slide 10: Three Meanings of “YANG”
10

## Slide 11: YANG Modeling Language
Module that is a self-contained top-level hierarchy of nodes
Uses containers to group related nodes (On most of the cases it contains Configuration details or operation details)
Lists to identify nodes that are stored in sequence
Each individual attribute of a node is represented by a leaf (Leaf is a unique piece of information)
Every leaf must have an associated type ( In below example Boolean)
11
module ietf-interfaces { import ietf-yang-types {
prefix yang;
}
container interfaces { list interface {
key "name";
leaf name { type string;
}
leaf enabled { type boolean; default "true";
}
}
Example edited for simplicity and brevity

## Slide 12: What is a Data Model?
A data model is simply a well understood and agreed upon method to describe "something". As an example, consider this simple "data model" for a person.
12
Person
  Gender - male, female, other
  Height - Feet/Inches or Meters
  Weight - Pounds or Kilos
  Hair Color - Brown, Blond, Black, Red, other
  Eye Color - Brown, Blue, Green, Hazel, other

## Slide 13: What might a YANG Data Model describe?
Device Data Models
Interface
VLAN
Device ACL
Tunnel
OSPF
etc
Service Data Model
L3 MPLS VPN
MP-BGP
Network ACL
EVPN
System Management
Network Faults
etc
13

## Slide 14: Working with YANG Data Models

## Slide 15: Where do Models Come From?
Standard definition
(IETF, ITU, OpenConfig, etc.)
Compliant with standard
ietf-diffserv-policy.yang ietf-diffserv-classifer.yang ietf-diffserv-target.yang
Industry Standard
Vendor Specific
Vendor definition
(i.e. Cisco)
Unique to Vendor Platforms cisco-memory-stats.yang cisco-flow-monitor
cisco-qos-action-qlimit-cfg
https://github.com/YangModels/yang

## Slide 16: What is OpenConfig?
Models Designed by Operators for Operators
“OpenConfig’s initial focus is on compiling a consistent set of vendor- neutral data models based on actual operational needs from use cases and requirements from multiple network operators.”
OpenConfig FAQ: www.openconfig.com

## Slide 17: What is OpenConfig?
Models Designed by Operators for Operators
Focused on creating vendor-neutral data models written in YANG
Models combine both configuration and operational data
Model coverage still limited with an active development community
Support from multiple routing vendors (e.g. Cisco, Juniper, Arista)
  Vendor exceptions carried a deviations

## Slide 18: Where to get the Models?
For YANG modules from standard organizations such as the IETF, open source such as Open Daylight or vendor specific modules”
  https://github.com/YangModels/yang
For OpenConfig models
  https://github.com/openconfig/public

## Slide 19: YANG Data Models
The model can be displayed and represented in any number of formats depending on needs at the time. Some options include:
YANG Language
Clear Text
XML
JSON
HTML/JavaScript

## Slide 20: Working with YANG Models
Example output edited for simplicity and brevity
DevNet$ pyang –f tree ietf-interfaces.yang
module: ietf-interfaces
+--rw interfaces
¦ | +--rw interface* [name] | 
¦ | +--rw name | string
¦ | +--rw description? | string
¦ | +--rw type | identityref
¦ | +--rw enabled? | boolean
¦ | +--rw link-up-down-trap-enable? | enumeration {if-mib}?

## Slide 21: Using pyang
Python YANG Library
Validate and display YANG files
Many formats for display
  Text: tree
  HTML: jstree

## Slide 22: Augmentation and Deviations in YANG
Standard Model
Standard Model with Augmentation
Standard Model with
Deviation

## Slide 23: Actual Device Data Modeled in YANG

## Slide 24: Use NETCONF to Retrieve ietf-interfaces data
from device_info import ios_xe1 from ncclient import manager import xml.dom.minidom
# NETCONF filter to use
netconf_filter = open("filter-ietf-interfaces.xml").read()
if name == ' main ':
with manager.connect(host=ios_xe1["address"],
port=ios_xe1["port"], username=ios_xe1["username"], password=ios_xe1["password"], hostkey_verify=False) as m:
netconf_reply = m.get_config("running", netconf_filter) interfaces = xml.dom.minidom.parseString(netconf_reply.xml) interfaces = interfaces.getElementsByTagName("interfaces") print(interfaces[0].toprettyxml())
NETCONF details covered in another session
ncclient provides a Python client for NETCONF
Using built-in library to print reply
  xml.dom.minidom

## Slide 25: Use NETCONF to Retrieve ietf-interfaces data
<description>DON'T TOUCH ME</description>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if-type">ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
<ipv4 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip">
<address>
<ip>10.10.10.48</ip>
<netmask>255.255.255.0</netmask>
</address>
</ipv4>
<ipv6 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip"/>
</interface>
<interface>
<name>GigabitEthernet2</name>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if-type">ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
<ipv4 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip"/>
<ipv6 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip"/>
</interface>
</interfaces>

## Slide 26: YANG Model Augmentation
(venv) $pyang -f tree ietf-interfaces.yang module: ietf-interfaces
+--rw interfaces
| +--rw interface* [name]
| +--rw name
string
¦ | +--rw | description? | string
¦ | +--rw | type | identityref
¦ | +--rw | enabled? | boolean
¦ | +--rw | link-up-down-trap-enable? | enumeration {if-mib}?
<ip>172.16.20.1</ip>
<interface>
<name>GigabitEthernet2</name>
<description>**THIS IS INTERFACE 2**</description>
<type>ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
<ipv4 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip">
<address>
<netmask>255.255.255.0</netmask>
</address>
</ipv4>
</interface>
Where is the <ipv4> leaf in the model?
The YANG model states what base model it is augmenting.
module: ietf-ip |  |  | 
 | augment /if:interfaces/if:interface: |  | 
+--rw ipv4! ¦ +--rw enabled? boolean ¦ +--rw forwarding? boolean ¦ +--rw mtu? uint16 ¦ +--rw address* [ip] ¦ ¦ +--rw ip inet:ipv4-address-no-zone ¦ ¦ +--rw (subnet) ¦ ¦ +--:(prefix-length) ¦ ¦ ¦ +--rw prefix-length? uint8 ¦ ¦ +--:(netmask) ¦ ¦ +--rw netmask? yang:dotted-quad {ipv4-non-contiguous-netmasks}? |  |  | 

## Slide 27: YANG Model Deviations
<interfaces-state xmlns="ietf-interfaces">
<interface>
<name>GigabitEthernet1</name>
<type>ianaift:ethernetCsmacd</type>
<admin-status>up</admin-status>
<oper-status>up</oper-status>
<last-change>2017-11-14T13:33:</last-change>
<if-index>0</if-index>
<phys-address>00:50:56:bb:c9:2c</phys-address>
<speed>1024000</speed>
<statistics>
<discontinuity-time>..</discontinuity-time>
<in-octets>41705747838</in-octets>
<in-unicast-pkts>129128494</in-unicast-pkts>
<in-broadcast-pkts>0</in-broadcast-pkts>
<in-multicast-pkts>0</in-multicast-pkts>
<in-discards>0</in-discards>
<in-errors>0</in-errors>
<in-unknown-protos>0</in-unknown-protos>
<out-octets>168135978</out-octets>
<out-unicast-pkts>414310</out-unicast-pkts>
<out-broadcast-pkts>0</out-broadcast-pkts>
<out-multicast-pkts>0</out-multicast-pkts>
<out-discards>0</out-discards>
<out-errors>0</out-errors>
</statistics>
</interface>
</interfaces-state>
Outputs modified for screen display
module: ietf-ip
augment /if:interfaces-state/if:interface:
+--ro ipv4!
+--ro address* [ip]
| +--ro ip inet:ipv4-address-no-zone
| +--ro (subnet)?
| | +--:(prefix-length)
| | | +--ro prefix-length? uint8
| | +--:(netmask)
| | +--ro netmask?
| +--ro forwarding? boolean
| +--ro mtu? uint16
|
|
|
|
|
|
|
|
| +--ro origin?
yang:dotted-quad ip-address-origin
Where is the <ipv4> leaf in the device data?

## Slide 28: YANG Model Deviations
<interfaces-state xmlns="ietf-interfaces">
<interface>
<name>GigabitEthernet1</name>
<type>ianaift:ethernetCsmacd</type>
<admin-status>up</admin-status>
<oper-status>up</oper-status>
<last-change>2017-11-14T13:33:</last-change>
<if-index>0</if-index>
<phys-address>00:50:56:bb:c9:2c</phys-address>
<speed>1024000</speed>
<statistics>
<discontinuity-time>..</discontinuity-time>
<in-octets>41705747838</in-octets>
<in-unicast-pkts>129128494</in-unicast-pkts>
<in-broadcast-pkts>0</in-broadcast-pkts>
<in-multicast-pkts>0</in-multicast-pkts>
<in-discards>0</in-discards>
<in-errors>0</in-errors>
<in-unknown-protos>0</in-unknown-protos>
<out-octets>168135978</out-octets>
<out-unicast-pkts>414310</out-unicast-pkts>
<out-broadcast-pkts>0</out-broadcast-pkts>
<out-multicast-pkts>0</out-multicast-pkts>
<out-discards>0</out-discards>
<out-errors>0</out-errors>
</statistics>
</interface>
</interfaces-state>
Outputs modified for screen display
module: ietf-ip
augment /if:interfaces-state/if:interface:
+--ro ipv4!
uint16
inet:ipv4-address-no-zone
| +--:(prefix-length)
| | +--ro prefix-length? uint8
| +--:(netmask)
| +--ro netmask?
| +--ro forwarding? boolean
| +--ro mtu?
| +--ro address* [ip]
| | +--ro ip
| | +--ro (subnet)?
| |
| |
| |
| |
| |
+--ro origin?
yang:dotted-quad ip-address-origin
module cisco-xe-ietf-ip-deviation { namespace "http://cisco.com/ns/cisco-xe-ietf-ip-deviation"; . . | 
 | deviation /if:interfaces-state/if:interface/ip:ipv4{ deviate not-supported; description "Not supported in IOS-XE"; }
} | 
Where is the <ipv4> leaf in the device data?
YANG deviations allow for vendors to modify from standard models when required.

## Slide 29: YANG Summary

## Slide 30: YANG Summary
YANG is a Data Modeling Language
YANG Modules are constructed to create standard data models for network data
YANG Data sent to or from a network device will be formatted in either XML or JSON depending on the protocol (ex: NETCONF or RESTCONF)
34

## Slide 31: Understanding NETCONF
NETCONF is the protocol that applies the changes to the relevant datastore upon the device.

## Slide 32: Introducing the NETCONF Protocol
Some key details:
Initial standard in 2006 with RFC4741
Latest standard
is RFC6241 in 2011
Does NOT explicitly define content

## Slide 33: NETCONF Protocol Stack

## Slide 34: Transport - SSH
$ ssh admin@192.168.0.1 -p 830 -s netconf
admin@192.168.0.1's password:
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.1</capability>
<capability>urn:ietf:params:netconf:capability:candidate:1.0</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-netconf-monitoring</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-interfaces</capability> [output omitted and edited for clarity]
</capabilities>
<session-id>19150</session-id></hello>]]>]]>
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.0</capability>
</capabilities>
</hello>]]>]]>
Client (Manager) sends hello
Example edited for simplicity and brevity
SSH Login
Server (Agent) sends hello

## Slide 35
Transport - SSH
$ ssh admin@192.168.0.1 -p 830 -s netconf admin@192.168.0.1's password: SSH Login
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.1</capability>
<capability>urn:ietf:params:netconf:capability:candidate:1.0</capability> Server (Agent)
<capability>urn:ietf:params:xml:ns:yang:ietf-netconf-monitoring</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-interfaces</capability> sends hello
[output omitted and edited for clarity]
</capabilities>
<session-id>19150</session-id></hello>]]>]]>
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0"> Client (Manager)
<capabilities> sends hello
<capability>urn:ietf:params:netconf:base:1.0</capability>
</capabilities> Example edited for simplicity and brevity
</hello>]]>]]>
Don’t NETCONF Like this!

## Slide 36: Messages - Remote Procedure Call (RPC)

## Slide 37: Operations - NETCONF Actions
Operation | Description
<get> | Retrieve running configuration and device state information
<get-config> | Retrieve all or part of specified configuration data store
<edit-config> | Loads all or part of a configuration to the specified configuration data store
<copy-config> | Replace an entire configuration data store with another
<delete-config> | Delete a configuration data store
<commit> | Copy candidate data store to running data store
<lock> / <unlock> | Lock or unlock the entire configuration data store system
<close-session> | Graceful termination of NETCONF session
<kill-session> | Forced termination of NETCONF session

## Slide 38: Additional Operations
The IETF isn’t able to anticipate every use case from every vendor.
Additional operations can be defined by the vendor
Support extended through RPC call to vendor-specific YANG model
write mem?
commit
?
copy run start?

## Slide 39: NETCONF Data Stores
Data Store Key Points
Entire or partial configuration
"running" is the only mandatory data store
Not all data stores are writeable
A "URL" data store is supported by IOS to enable <config-copy>
Every NETCONF message must target a data store
result = m.get_config('running')

## Slide 40: NETCONF Communications

## Slide 41: NETCONF in Code with Python

## Slide 42: NETCONF and Python: ncclient
Full NETCONF Manager implementation in Python
  https://ncclient.readthedocs.io
Simplifies connection and communication.
Deals in raw XML
ncclient – Will list the capability
From: http://ncclient.readthedocs.io/en/latest/
from ncclient import manager
m = manager.connect(host="192.168.0.1",
port=830, username="admin", password="cisco123", hostkey_verify=False
)
m.close_session()

## Slide 43: Saying <hello> with Python and ncclient
from device_info import ios_xe1 from ncclient import manager
if name == ' main ':
with manager.connect(host=ios_xe1["address"],
port=ios_xe1["port"], username=ios_xe1["username"], password=ios_xe1["password"], hostkey_verify=False) as m:
print("Here are the NETCONF Capabilities") for capability in m.server_capabilities:
print(capability)
example1.py: Saying
<hello>
manager.connect() opens NETCONF session with device
  Parameters: host & port, user & password
  hostkey_verify=False
Trust cert
Stores capabilities

## Slide 44: Understanding the Capabilities List
DevNet$ python example1.py
Here are the NETCONF Capabilities
urn:ietf:params:netconf:base:1.0 urn:ietf:params:netconf:base:1.1
.
urn:ietf:params:xml:ns:yang:ietf-interfaces?module=ietf-interfaces&revision=2014-05-08&features=pre- provisioning,if-mib,arbitrary-names&deviations=ietf-ip-devs
http://cisco.com/ns/ietf-ip/devs?module=ietf-ip-devs&revision=2016-08-10
http://cisco.com/ns/yang/Cisco-IOS-XE-native?module=Cisco-IOS-XE-native&revision=2017-02-07
Two General Types
Base NETCONF capabilities
Data Models Supported
y

## Slide 45: Understanding the Capabilities List
urn:ietf:params:xml:ns:yang:ietf-interfaces
? module=ietf-interfaces & revision=2014-05-08
& features=pre-provisioning,if-mib,arbitrary-names & deviations=ietf-ip-devs
.
http://cisco.com/ns/ietf-ip/devs
? module=ietf-ip-devs & revision=2016-08-10
Data Model Details
Model URI
Module Name and Revision Date
Protocol Features
Deviations – Another model that modifies this one
Example edited for simplicity and brevity

## Slide 46: Automate Network with NETCONF

## Slide 47: Getting Interface Details with XML Filter
from device_info import ios_xe1 from ncclient import manager import xmltodict
print(" print(" print(" print(" print(" print("
# NETCONF filter to use
netconf_filter = open("filter-ietf-interfaces.xml").read()
if name == ' main ':
with manager.connect(host=ios_xe1["address"],
port=ios_xe1["port"], username=ios_xe1["username"], password=ios_xe1["password"], hostkey_verify=False) as m:
# Get Configuration and State Info for Interface
netconf_reply = m.get(netconf_filter)
# Process the XML and store in useful dictionaries
intf_details = xmltodict.parse(netconf_reply.xml)["rpc-reply"]["data"] intf_config = intf_details["interfaces"]["interface"]
intf_info = intf_details["interfaces-state"]["interface"]
print("")
print("Interface Details:")
Name: {}".format(intf_config["name"]))
Description: {}".format(intf_config["description"])) Type: {}".format(intf_config["type"]["#text"]))
MAC Address: {}".format(intf_info["phys-address"]))
Packets Input: {}".format(intf_info["statistics"]["in-unicast-pkts"])) Packets Output: {}".format(intf_info["statistics"]["out-unicast-pkts"]))
example2.py: Retrieving info with ncclient
Send <get> to retrieve config and state data
Process and leverage XML within Python
Report back current state of interface

## Slide 48: Getting Interface Details with XML Filter
example2.py: Retrieving info with ncclient
Send <get> to retrieve config and state data
Process and leverage XML within Python
Report back current state of interface
<filter>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>GigabitEthernet2</name>
</interface>
</interfaces>
<interfaces-state xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>GigabitEthernet2</name>
</interface>
</interfaces-state>
</filter>

## Slide 49: Getting Interface Details with XML Filter
from device_info import ios_xe1 from ncclient import manager import xmltodict
print(" print(" print(" print(" print(" print("
# NETCONF filter to use
netconf_filter = open("filter-ietf-interfaces.xml").read()
if name == ' main ':
with manager.connect(host=ios_xe1["address"],
port=ios_xe1["port"], username=ios_xe1["username"], password=ios_xe1["password"], hostkey_verify=False) as m:
# Get Configuration and State Info for Interface
netconf_reply = m.get(netconf_filter)
# Process the XML and store in useful dictionaries
intf_details = xmltodict.parse(netconf_reply.xml)["rpc-reply"]["data"] intf_config = intf_details["interfaces"]["interface"]
intf_info = intf_details["interfaces-state"]["interface"]
print("")
print("Interface Details:")
Name: {}".format(intf_config["name"]))
Description: {}".format(intf_config["description"])) Type: {}".format(intf_config["type"]["#text"]))
MAC Address: {}".format(intf_info["phys-address"]))
Packets Input: {}".format(intf_info["statistics"]["in-unicast-pkts"])) Packets Output: {}".format(intf_info["statistics"]["out-unicast-pkts"]))
example2.py: Retrieving info with ncclient
Send <get> to retrieve config and state data
Process and leverage XML within Python
Report back current state of interface

## Slide 50: Getting Interface Details
DevNet$ python example2.py
Interface Details:
Name: GigabitEthernet2 Description: DON'T TOUCH ME Type: ianaift:ethernetCsmacd MAC Address: 00:50:56:bb:74:d5 Packets Input: 592268689
Packets Output: 21839

## Slide 51: Getting Interface Details with XPath
example3.py: Retrieving info with ncclient and XPath
Send <get> to retrieve and state data
Process the data
Report back current state of interface
DevNet$python example3.py
Interface Details:
Name: GigabitEthernet1 Packets Output: 415200
from device_info import ios_xe1 from ncclient import manager import xmltodict
if name == ' main ':
with manager.connect(host=ios_xe1["address"],
port=ios_xe1["port"], username=ios_xe1["username"], password=ios_xe1["password"], hostkey_verify=False) as m:
# Get Configuration and State Info for Interface
netconf_reply = m.get(filter=('xpath' ,
"/interfaces-state/interface[name='GigabitEthernet1']" "/statistics/out-unicast-pkts"))
intf_details = xmltodict.parse(netconf_reply.xml)["rpc-reply"]["data"] intf_info = intf_details["interfaces-state"]["interface"]
print("")
print("Interface Details:")
print(" Name: {}".format(intf_info["name"]))
print(" Packets Output: {}".format(intf_info["statistics"]["out-unicast-pkts"]))

## Slide 52: Configuring Interface Details
from device_info import ios_xe1 from ncclient import manager
# NETCONF Config Template to use
netconf_template = open("config-temp-ietf-interfaces.xml").read()
if name == ' main ':
# Build the XML Configuration to Send
netconf_payload = netconf_template.format(int_name="GigabitEthernet2",
int_desc="Configured by NETCONF", ip_address="10.255.255.1", subnet_mask="255.255.255.0"
)
print("Configuration Payload:") print(" ")
print(netconf_payload)
with manager.connect(host=ios_xe1["address"], port=ios_xe1["port"],
username=ios_xe1["username"], password=ios_xe1["password"], hostkey_verify=False) as m:
# Send NETCONF <edit-config>
netconf_reply = m.edit_config(netconf_payload, target="running")
# Print the NETCONF Reply
print(netconf_reply)
example4.py: Editing configuration with ncclient
Constructing XML Config Payload for NETCONF
Sending <edit-config> operation with ncclient
Verify result

## Slide 53: Configuring Interface Details
example4.py: Editing configuration with ncclient
Constructing XML Config Payload for NETCONF
Sending <edit-config> operation with ncclient
Verify result
config-temp-ietf-interfaces.xml
<name>{int_name}</name>
<config>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<description>{int_desc}</description>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if-type">ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
<ipv4 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip">
<address>
<ip>{ip_address}</ip>
<netmask>{subnet_mask}</netmask>
</address>
</ipv4>
</interface>
</interfaces>
</config>
if name == ' main ':
# Build the XML Configuration to Send
netconf_payload =
netconf_template.format(int_name="GigabitEthernet2",
int_desc="Configured by NETCONF", ip_address="10.255.255.1", subnet_mask="255.255.255.0"
)
print("Configuration Payload:") print(" ") print(netconf_payload)

## Slide 54: Configuring Interface Details
from device_info import ios_xe1 from ncclient import manager
# NETCONF Config Template to use
netconf_template = open("config-temp-ietf-interfaces.xml").read()
if name == ' main ':
# Build the XML Configuration to Send
netconf_payload = netconf_template.format(int_name="GigabitEthernet2",
int_desc="Configured by NETCONF", ip_address="10.255.255.1", subnet_mask="255.255.255.0"
)
print("Configuration Payload:") print("----------------------")
print(netconf_payload)
with manager.connect(host=ios_xe1["address"], port=ios_xe1["port"],
username=ios_xe1["username"], password=ios_xe1["password"], hostkey_verify=False) as m:
# Send NETCONF <edit-config>
netconf_reply = m.edit_config(netconf_payload, target="running")
# Print the NETCONF Reply
print(netconf_reply)
example4.py: Editing configuration with ncclient
Constructing XML Config Payload for NETCONF
Sending <edit-config> operation with ncclient
Verify result

## Slide 55: Configuring Interface Details
DevNet$ python -i example4.py Configuration Payload:
<config>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>GigabitEthernet2</name>
<description>Configured by NETCONF</description>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if-type"> ianaift:ethernetCsmacd
</type>
<enabled>true</enabled>
<ipv4 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip">
<address>
<ip>10.255.255.1</ip>
<netmask>255.255.255.0</netmask>
</address>
</ipv4>
</interface>
</interfaces>
</config>
<?xml version="1.0" encoding="UTF-8"?>
<rpc-reply xmlns=”urn.." message-id=”..9784" xmlns:nc="urn..">
<ok/>
</rpc-reply>
Example edited for simplicity and brevity

## Slide 56: Saving Running Configuration with ncclient
from device_info import ios_xe1 from ncclient import manager, xml_
if name == ' main ':
with manager.connect(host=ios_xe1["address"],
port=ios_xe1["port"], username=ios_xe1["username"], password=ios_xe1["password"], hostkey_verify=False) as m:
# Build XML Payload for the RPC
save_body = '<cisco-ia:save-config xmlns:cisco-ia="http://cisco.com/yang/cisco-ia"/>'
# Send the RPC to the Device
save_rpc = m.dispatch(xml_.to_ele(save_body))
# Print the NETCONF Reply
print(save_rpc)
example5.py: Save running configuration with ncclient
Constructing XML Config Payload for NETCONF
Sending custom save operation with ncclient
Verify result
60

## Slide 57: Saving Running Configuration with ncclient
61
<result xmlns='http://cisco.com/yang/cisco-ia'>
Save running-config successful
</result>
<?xml version="1.0" encoding="UTF-8"?>
<rpc-reply xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="urn:uuid:d12c3cc5-f638-499e-9e57-c8d2402fdfeb" xmlns:nc="urn:ietf:params:xml:ns:netconf:base:1.0">
</rpc-reply>

## Slide 58: NETCONF Summary

## Slide 59: NETCONF Summary
The elements of the NETCONF transport protocol
How to leverage ncclient to use NETCONF in Python
Examples retrieving and configuring data from a NETCONF Agent
63

## Slide 60: Understanding RESTCONF

## Slide 61: RESTCONF Details
“an HTTP-based protocol that provides a programmatic interface for accessing data defined in YANG…”
https://tools.ietf.org/html/rfc8040
RFC 8040 - January 2017
Uses HTTPS for transport
Tightly coupled to the YANG data model definitions
Provides JSON or XML data formats

## Slide 62: What about NETCONF?

## Slide 63: RESTCONF Protocol Stack & Transport

## Slide 64: Operations - HTTP CRUD
RESTCONF | NETCONF
GET | <get> , <get-config>
POST | <edit-config> (operation="create")
PUT | <edit-config> (operation="create/replace")
PATCH | <edit-config> (operation="merge")
DELETE | <edit-config> (operation="delete")

## Slide 65: Content - XML or JSON
HTTP Headers
Content-Type: Specify the type of data being sent from the client
Accept: Specify the type of data being requested by the client
RESTCONF MIME Types
application/yang-data+json
application/yang-data+xml

## Slide 66: Constructing RESTCONF URIs for Data Resources
https://<ADDRESS>/<ROOT>/data/<[YANG MODULE:]CONTAINER>/<LEAF>[?<OPTIONS>]
ADDRESS - Of the RESTCONF Agent
ROOT - The main entry point for RESTCONF requests. Discoverable at https://<ADDRESS>/.well-known/host-meta
data - The RESTCONF API resource type for data
  The “operations” resource type used to access RPC operations available
[YANG MODULE:]CONTAINER - The base model container being used. Providing the module name is optional.
LEAF - An individual element from within the container
[?<OPTIONS>] - optional parameters that impact returned results.

## Slide 67: URL Creation Review
https://<ADDRESS>/restconf/data/ietf-interfaces:interfaces/interface=GigabitEthernet1?depth=unbounded
module: ietf-interfaces
+--rw interfaces
¦ | +--rw interface* [name] | 
¦ | +--rw name | string
¦ | +--rw description? | string
¦ | +--rw type | identityref
¦ | +--rw enabled? | boolean
¦ | +--rw link-up-down-trap-enable? | enumeration
{if-mib}?
Options Examples:
depth=unbounded
Follow nested models to end. Integer also supported
content=[all, config, nonconfig]
Query option controls type of data returned.
fields=expr
Limit what leafs are returned
Key:
https://<ADDRESS>/<ROOT>/data>/<[YANG MODULE:]CONTAINER>/<LEAF>[?<OPTIONS>]

## Slide 68: Using RESTCONF with Postman

## Slide 69: Postman: Powerful but Simple REST API Client
Quickly test APIs in GUI
Save APIs into Collections for reuse
Manage multiple environments
Auto generate code from API calls
https://www.getpostman.com

## Slide 70: Setup Environment for RESTCONF
Add variables for host, and credentials
Reference anywhere with {{variable name}} syntax

## Slide 71: Step 1: Get YANG Modules List via RESTCONF
GET /restconf/data/ietf-yang-library:modules-state
Add RESTCONF Headers
  Content-Type and Accept application/yang-data+json (or xml)
Configure Basic Auth with username and password variables
Example –
• CSR1000V Host: ios-xe-mgmt.cisco.com ◦ RESTCONF Ports: 9443 (HTTPS) • Username: developer • Password: C1sco12345
https://64.103.37.51:9443/restconf/data/ietf-yang-library:modules-state

## Slide 72: Step 1: Get YANG Modules List via RESTCONF
Send and review results

## Slide 73: Understanding the YANG Modules List
Data Model Details
Model URI
Module Name and Revision Date
Protocol Features
Deviations – Another model that modifies this one
{"ietf-yang-library:modules-state": {"module": [
{
"name": "ietf-ip",
"revision": "2014-06-16",
"schema": "https://10.10.20.48:443/restconf/tailf/..", "namespace": "urn:ietf:params:xml:ns:yang:ietf-ip", "feature": [
"ipv6-privacy-autoconf", "ipv4-non-contiguous-netmasks"
],
"deviation": [
{
"name": "cisco-xe-ietf-ip-deviation", "revision": "2016-08-10"
}
],
"conformance-type": "implement"
},
{
"name": "cisco-xe-ietf-ip-deviation", "revision": "2016-08-10",
"schema": "https://10.10.20.48:443/restconf/tailf/...", "namespace": "http://cisco.com/ns/cisco-xe-ietf-ip-deviation", "conformance-type": "implement"
}]}}

## Slide 74: Automate Network with RESTCONF

## Slide 75: Getting Interface Details
GET
restconf/data/ietf-interfaces:interfaces/interface=GigabitEthernet2
Configure Auth and Headers

## Slide 76: Configuring Interface Details
PUT
restconf/data/ietf-interfaces:interfaces/interface=GigabitEthernet2
Configure Auth and Headers
Configure Body (raw)
Send and check status code

## Slide 77: Configuring Interface Details - Verification
GET
restconf/data/ietf-interfaces:interfaces/interface=GigabitEthernet2
Configure Auth and Headers
Check that the new config was successful

## Slide 78: Save Running Configuration to Startup RPC Operation
POST
restconf/operations/cisco-ia:save-config/
Configure Auth and Headers

## Slide 79: RESTCONF with Python

## Slide 80: Python Libraries for RESTCONF
Treat like other “REST” and HTTP APIs
Core Python Library
  urllib (urllib.request)
Other HTTP Library
  Requests: http for humans
84

## Slide 81: RESTCONF and HTTPS/SSL
Per RFC8040 RESTCONF requires HTTPS for security
HTTPS leverages SSL/TLS certificates to
  Encrypt data transmitted between server and client
  Verify a sites identity
Encryption accomplished through Private/Public keys in Certificate
Identity is all about “trust” and the “signer” of a certificate
85

## Slide 82: Self-Signed SSL Certificates are Common
No problems with encryption
“Trust” fails due to no Certificate Authority
Common in most of our daily lives
  Network web GUIs
  Internal corporate web sites
  Poorly managed company sites
Knee-jerk reaction to click “Accept” or “Proceed”
86

## Slide 83: “Accepting” Self-Signed Certificates with Python Requests
Requests (via urllib) performs SSL Validation by default
response = requests.get(url, auth=("root", "D_Vay!_10&"))
>>> import requests
>>> url = "https://ios-xe-mgmt.cisco.com:9443/.well-known/host-meta"
>>>
Traceback (most recent call last):
File "<pyshell#7>", line 1, in <module>
response = requests.get(url, auth=("root", "D_Vay!_10&"))
SSLError: HTTPSConnectionPool(host='ios-xe-mgmt.cisco.com', port=9443): Max retries exceeded with url: /.well-known/host-meta (Caused by SSLError(SSLError(1, u'[SSL: CERTIFICATE_VERIFY_FAILED]
certificate verify failed (_ssl.c:661)'),))
87

## Slide 84: “Accepting” Self-Signed Certificates with Python Requests
Disable with
verify = False
Still generates a Warning notification
But the request is successful
>>> import requests >>> url = "https://ios-xe-mgmt.cisco.com:9443/.well-known/host-meta" >>> response = requests.get(url, auth=("root", "D_Vay!_10&"), verify=False) Warning (from warnings module): File "/Users/hapresto/coding/BRKDEV-1368/venv/lib/python2.7/site- packages/urllib3/connectionpool.py", line 858 InsecureRequestWarning) InsecureRequestWarning: Unverified HTTPS request is being made. Adding certificate verification is strongly advised. See: https://urllib3.readthedocs.io/en/latest/advanced-usage.html#ssl-warnings | 
>>> print(response.text) <XRD xmlns='http://docs.oasis-open.org/ns/xri/xrd-1.0'> <Link rel='restconf' href='/restconf'/> </XRD> | 
88

## Slide 85: Disabling Insecure SSL Warnings from urllib
Import urllib
Disable warnings
>>> requests.packages.urllib3.disable_warnings()
>>> response = requests.get(url, auth=("root", "D_Vay!_10&"), verify=False)
>>> print(response.text)
<XRD xmlns='http://docs.oasis-open.org/ns/xri/xrd-1.0'>
<Link rel='restconf' href='/restconf'/>
</XRD>
89

## Slide 86: RESTCONF in Python
# Used to configure the IP address on an interface
def configure_ip_address(interface, ip):
# RESTCONF URL for specific interface
url = url_base + "/data/ietf-interfaces:interfaces/interface={i}".format(i=interface)
90
# Create the data payload to reconfigure IP address
# Need to use OrderedDicts to maintain the order of elements
data = OrderedDict([('ietf-interfaces:interface', OrderedDict([
('name', interface),
('type', 'iana-if-type:ethernetCsmacd'), ('ietf-ip:ipv4',
OrderedDict([
('address', [OrderedDict([ ('ip', ip["address"]),
('netmask', ip["mask"])
])]
)
])
),
])
)])
# Use PUT request to update data
response = requests.put(url,
auth=(USER, PASS),
headers=headers, verify=False, json=data
)
print(response.text)
Example function to configure IP with RESTCONF
Using “requests”

## Slide 87: Is RESTCONF a REST API?
It depends…
(of course it does)
91

## Slide 88: Richardson Maturity Model for REST
RESTCONF is a Level 2 REST API
RESTCONF targets resources
RESTCONF uses HTTP Verbs
RESTCONF doesn’t use Hypermedia Controls
Source: https://martinfowler.com/articles/richardsonMaturityModel.html
92

## Slide 89: RESTCONF Summary

## Slide 90: Review
© 2020 Cisco and/or its affiliates. All rights reserved. Cisco Public
The elements of the RESTCONF transport protocol
How to leverage Postman to use RESTCONF
Examples retrieving and configuring data using RESTCONF
Yep, RESTCONF is a REST API!
94
BRKDEV-1368

## Slide 91: DEMO

## Slide 92: Questions?

## Slide 93: What do do next?
Resources
  Overview of the 2002 IAB Network Management Workshop
  Network Configuration Protocol (NETCONF)
  The YANG 1.1 Data Modeling Language
  RESTCONF Protocol
  YANG Development Kit (YDK)
DevNet Learning Labs
  Introduction to Device Level Interfaces - NETCONF/YANG
  NETCONF/YANG on Nexus
  Home Lab: Using NETCONF/YANG from your Desktop OS
Blogs and Videos
  Using CLI as Training Wheels with NETCONF/YANG
  Simplifying Network Programmability with Model Driven APIs
  Network Device APIs Video Lessons

## Slide 94: References
BRKDEV-1368 by Hank Preston